|  | DEPARTMENT OF DEFENSE REGIONAL COMMAND SOUTH, COALITION TASK FORCE AEGIS ZABUL PROVINCIAL RECONSTRUCTION TEAM ZABUL PROVINCE, AFGHANISTAN |
| --- | --- |

19Mar09

PURPOSE:   		Statement of Work

PROJECT:  	 	Zabul Provencial Medical Conexes

CUSTOMER:		Zabul Provincial Reconstruction Team (PRT)

Zabul Province, Afghanistan

APO AE 09355

CONTRACTOR:  	Name: TBD

Address: TBD

Phone: TBD

- Scope:

Project

Afghanistan is ranked #10 in the world for most favorable conditions for solar cooking and has over 300 sunny days annually.  This project is designed to use these strengths and promote the UN Millenial Developmental Goals and the objectives of the ANDS.

According to the UN Millenial Developmental Goals, goal number 7 is to ensure environmental sustainability.  The ANDS sets targets for nutrition, public health, and economic/private sector development.  Afghanistan has a limited supply of fuel, its landscape heavily deforested, and its people find it extremely difficult to obtain/buy fuel.  The cooking process inside the homes exposes the families to unhealthy fumes and multiple injuries are acquired during this process.  Based on the above goals, the situation in Afghanistan, and the favorable environment for solar cooking the Zabul PRT proposes to conduct a pilot project using this technology.

Solar cooking in Afghanistan has a tradition from many refugee camps and several NGO’s working here.  The most successful and appropriate solar cooking apparatus to date in Afghanistan is from Kabul, where an NGO has developed a way to produce solar cookers from all local materials and distribute them.  They have been successful in selling them for cost, as the demand for these cookers in Kabul has increased with public knowledge.  These cookers are best suited for Afghanistan because they heat up fast and cook hot; they are able to cook traditional Afghan meals using Afghan pressure cookers.  The Zabul PRT proposes to use this successful model, learn from their expertise, and conduct a pilot program in Zabul.  Depending if the pilot program is successful will determine if this project expands into a larger private sector development project or not.

The below material list is what is required for producing each solar cooker and the total amounts of materials for 50 solar cookers.

Some pictures of the solar cooker and parts:

- Finished cooker working			b. back of cooker, metal stand

Projected costs to produce 50 solar cookers

| Part/Material/Labor | dimensions | total quantity | units | US dollars |
| --- | --- | --- | --- | --- |
| wire | 3mm diameter | 175 | kg | 245 |
| wire | 0.5mm diameter | 5 | kg | 7 |
| rebar | 8mm diameter | 1500 | meters | 170 |
| rebar | 12mm diameter | 1500 | meters | 227 |
| flat iron | 30cm length, 5cm width, 5mm thick | 50 | pieces | 40 |
| flat iron | 10cm length, 5cm width, 4mm thick | 50 | pieces | 20 |
| metal water pipe | 1/2 inch diameter (Russian) | 100 | meters | 170 |
| metal water pipe | slightly larger than 1/2 inch (Russian) | 20 | meters | 50 |
| metal water pipe | 1 inch diameter (Russian) | 60 | meters | 150 |
| metal water pipe | slightly larger than 1 inch (Russian) | 20 | meters | 70 |
| metal elbow pipe | 1/2 inch diameter | 50 | pieces | 10 |
| bolt & nuts | 12mm diameter, 4-5cm length | 150 | bolts/nuts | 30 |
| washed sand | (Maybe 1$ per dish) | 650 | shovels | 50 |
| gravel | pea sized | 150 | shovels | 25 |
| cement | 32 bags | 1600 | kg | 155 |
| bolt | 15-20mm diameter, 30-35cm length | 50 | bolts | 70 |
| nuts | to fit the above long bolt | 150 | nuts | 30 |
| wall putty | 3 L per dish (comes in 20L containers) | 150 | liters (8 containers) | 136 |
| sandpaper |  | 50 | packages | 30 |
| spatulas |  | 4 | spatulas | 4 |
| thin plastic sheets | 2m by 3m for each sheet | 25 | plastic sheets | 45 |
| reflective tape |  | 750 | dollars | 750 |
| sunglasses |  | 50 | sunglasses | 40 |
| black paint | (We will provide this à 3$ per litre) | 5 | cans | 15 |
| technical assistance | 1 week | 1 | training session | 500 |
| start up supplies | (include dirt, sand & cement for molds, to shape the dish-$100 & forms & template & wood pieces & tools) | 1 |  | 400 |
| welding machine |  | 0 |  |  |
| welding supplies |  | 0 |  |  |
| labor |  | 0 |  |  |
|  |  |  | Total Cost | 3439 |

- Delivery:

3.  Contract Amount and Payment Schedule: TBA after bidding session

4.  Details (see bid criteria for more details):

a.  	Upon NTP, the contractor will: Will purchase and transports the materials to the Qalat PRT

b.  	Once materials are received and verified by the PRT, the contractor will be paid for those supplies.

c.	Contractor is responsible for hiring and managing the labor required to produce these solar ovens

15. The Project Manager for the PRT physicians will be CAPT Brent Barnstuble, United States Air Force, who can be contacted at 0700905876 or by electronic mail at brent.b.barnstuble@us.swa.army.mil or bbarnstu@gmail.com.

Andrew Torelli, Lt Col, USAF

Commander, Zabul Provincial Reconstruction Team

For and on behalf of the Customer:

Dear Brent I calculated all numbers with 50 cookers, so just control it now.

Do you want to include anything for a welding machine, and for fuel, welding sticks, generator, etc? I am also not 100% sure about the cost of sand and gravel, you need to check that. About the reflective tape, we will provide you with enough tape for 50 cookers, with the price you mentioned. The tape we imported is hopefully good. However, we fixed some cookers and I think the damage was done by children or improper cleaning, with knifes, etc.. We had to replace this again. I hope it is because of improper cleaning and not because of bad tape (oxidizing). We also keep using this. If it goes bad, we will replace it.

If the tape gets dusty, etc, or has calcium build up from boiling water, it is best to clean with water/vinegar and a clean soft cloth.

Also you don’t have labor included to produce this cooker. If you want you can add some things to it like; teakettle ($4-each), mittens (done by ladies or widows $4 –pair), cover to protect cooker, can also be done by ladies: ($6 - each), up to you, we try to make it as affordable as possible and therefore just paint the pots the people bring. Also Grace has done an instruction booklet in Dari for another model, she will hopefully have adopted it soon to this cooker, these cost about 70cents per copy. (But we only have them in Dari!)

The reflective tape needs to be replaced after one to two years. Do you want to include this already in this proposal? We hope that as demand for cooker and public acceptance grows that this will create a need for a shop keeper, to import the reflective tape from China and to sell it. But we are not there yet. So we are still planning to import more tape for now.

I think it is important to make tape available for replacing in a year from now.